## Slide 1: Networking Basics For Applications

## Slide 2: Agenda
Outline the OSI model
Addressing
  Implement IPv4 addressing
  Understand network structures
  Discuss private networks and NAT translation
Multiplexing
  Port numbers and application management
  (Light MATH warning)
🚨 🚨

## Slide 3: Networking
Devices are more useful when they can talk to other devices
Very first connection  1940
Fledgling networks through 1960s-70s
ARPANET / ALOHA
Internetworks in late 70s
Research & commercial adoption
Today, billions of devices connected across billions of separate networks
Notes: https://en.wikipedia.org/wiki/Computer_network#/media/File:Internet_map_1024.jpg

## Slide 4: OSI model
Computer networks are complex
Desire to exchange network services based on needs
  Latency
  Bandwidth
  Reliability
  Mobility
 Separate functionality / roles into layers
Base concerns for application developers
  Multiplexing
  Addressing
  Reliability
Other layers important for troubleshooting issues
Notes: https://en.wikipedia.org/wiki/OSI_model

## Slide 5: A Brief Aside: Protocols
Ever interact with a protocol officer?
Protocols inform developers how to communicate
TTPs for software
  MUST, MUST NOT, SHOULD, SHOULD NOT
  Data types, formatting, extensibility
Common protocols
  Ethernet
  IP
  TCP
  UDP
  TLS/SSL
  HTTP
  SMTP
  FTP

## Slide 6: IPv4 Addressing

## Slide 7: IPv4 Addressing Basics
Addresses
4 octets of 8 binary digits (bits)  32 bits
  Expressed in dotted decimal notation
  192.168.0.1
  11000000 10101000 00000000 00000001
  Range of each octet is 0 – 255
A logical identifier for a device
  Each device can have multiple addresses
  In principle, each identifier is unique
Networks
Logical separation of address spaces
  Devices on the same network can talk directly (switched)
  Devices on separate networks need to be routed
Networks are defined by a “mask”
  The first N bits define the network portion
  The remaining 32 - N bits define the device ID
192.168.0.1 /24
  24 bits  network mask, last 8 bits  device mask
  11000000 10101000 00000000 00000001
  192.168.0.1 /24

## Slide 8: Binary Refresher
1 byte = 8 bits
Range = 0 – 255
Commonly the Most Significant Bit is on the left
Add up any value that has a `1` below it
  128 64 32 16 8 4 2 1
  0 1 1 0 0 0 0 0 (binary)
  64 + 32 = 96 (decimal)
32 bits = ?
  4,294,967,295 max

## Slide 9: IPv4 Addressing – More Networks
Work through some samples
  172. 20. 10. 5 /14
    10101100 00010100 00001010 00000101 (IP address)
    11111111 11111100 00000000 00000000 (network mask)
    10101100 00010100 00000000 00000000 (network addy)
    172.20.0.0
    00000000 00000011 11111111 11111111 (device mask)
    10101100 00010100 00001010 00000101 (device addy)
    172.20.10.5
  10. 12. 45.100 /16
  190.154. 10. 1 /12
  190.154. 30. 50 /12
  10. 65. 1. 20 /16
  172. 22. 5. 9 /14
Which addresses are on the same network?
How many devices addresses can be assigned in a /16?
Called “Classless InterDomain Routing” (CIDR)
Early internet was divided into “classes” of networks
  /8
  /12
  /16
CIDR enables more efficient subnetting
  190.154. 10. 1 /12
  190.154. 30. 50 /12
  172. 22. 5. 9 /14
  172. 20. 10. 5 /14
  10. 12. 45.100 /16
  10. 65. 1. 20 /16

## Slide 10
Notes: Subnetting allows us to split one larger network into multiple, smaller networks.

## Slide 11: IPv4 Addressing – Reserved Addresses
Network Range | Purpose
0.0.0.0/8 | Network identification, default routes
10.0.0.0/8 | Private networks (RFC 1918)
100.64.0.0/10 | Carrier-grade NAT (CGNAT)
127.0.0.0/8 | Loopback (localhost)
169.254.0.0/16 | Link-local (APIPA)
172.16.0.0/12 | Private networks (RFC 1918)
192.0.0.0/24 | IETF Protocol Assignments
192.168.0.0/16 | Private networks (RFC 1918)
192.88.99.0/24 | IPv6-to-IPv4 relay (deprecated)
198.18.0.0/15 | Network benchmark testing
224.0.0.0/4 | Multicast addresses
240.0.0.0/4 | Reserved for future use
255.255.255.255 | Limited broadcast

## Slide 12: IPv4 Addressing – Even More Networks
Different networks  needs routing
Internet consists of a “network of networks”
How do I prevent people from talking to devices on my network?
Didn’t we run out of IPv4 addresses?
Aren’t IP addresses expensive?

## Slide 13: IPv4 Addressing – NAT
To address some of these concerns, translation was introduced
  Usually the function of a router
  Convert external IP address into internal IP addresses
Types
  Static
  Dynamic
  PAT (NAT overload)

## Slide 14: Multiplexing

## Slide 15: Multiplexing
“having many folds; many times as great in number; of many parts”
Fitting multiple streams over the same channel
Transport layer handles this with ports (sits above network layer)
Each socket consists of an IP/port pair between sender and receiver
  Multiple streams of data on same interface
  Operating system needs to know where (which application) traffic should go

## Slide 16: Sockets
Scenario | Application | Source IP | Source Port | Dest IP | Dest Port | Socket Identifier (minus protocol)
Same App, Multiple Connections | Chrome (Tab 1) | 192.168.1.10 | 49152 | 142.250.185.46 | 443 | 192.168.1.10:49152 ↔ 142.250.185.46:443
 | Chrome (Tab 2) | 192.168.1.10 | 49153 | 142.250.185.46 | 443 | 192.168.1.10:49153 ↔ 142.250.185.46:443
Different Protocols | DNS Query | 192.168.1.10 | 51234 | 8.8.8.8 | 53 | 192.168.1.10:51234 ↔ 8.8.8.8:53
 | HTTPS Request | 192.168.1.10 | 51235 | 8.8.8.8 | 443 | 192.168.1.10:51235 ↔ 8.8.8.8:443
Same Dest Port, Different Services | Web Browser | 192.168.1.10 | 52001 | 93.184.216.34 | 80 | 192.168.1.10:52001 ↔ 93.184.216.34:80
 | FTP Client | 192.168.1.10 | 52002 | 93.184.216.34 | 21 | 192.168.1.10:52002 ↔ 93.184.216.34:21
Multiple Receivers | Email Client | 192.168.1.10 | 53001 | 74.125.200.108 | 993 | 192.168.1.10:53001 ↔ 74.125.200.108:993
 | Video Stream | 192.168.1.10 | 53002 | 151.101.1.140 | 443 | 192.168.1.10:53002 ↔ 151.101.1.140:443

## Slide 17: Port Reservations
When developing an application…
  Reserve an interface:port from the OS
  Connect to some other interface:port
  Use that socket to communicate
  Every separate data stream needs its own socket (in general)
    Different app
    Different source
    Different destination
  Often handled by lower-level libraries
  Cannot open a socket that another app is using
Python/powershell port demo

## Slide 18: IPv4 Addressing – PAT
Back to networking…

## Slide 19: PAT
Source IP | Source Port | Dest IP | Dest Port | Socket Identifier (minus protocol) | After PAT Rewrite
192.168.1.10 | 49152 | 142.250.185.46 | 443 | 192.168.1.10:49152 ↔ 142.250.185.46:443 | 203.0.113.50:50002 ↔ 142.250.185.46:443
192.168.1.10 | 49153 | 142.250.185.46 | 443 | 192.168.1.10:49153 ↔ 142.250.185.46:443 | 203.0.113.50:50003 ↔ 142.250.185.46:443
192.168.1.10 | 51234 | 8.8.8.8 | 53 | 192.168.1.10:51234 ↔ 8.8.8.8:53 | 203.0.113.50:50004 ↔ 8.8.8.8:53
192.168.1.10 | 51235 | 8.8.8.8 | 443 | 192.168.1.10:51235 ↔ 8.8.8.8:443 | 203.0.113.50:50005 ↔ 8.8.8.8:443
192.168.1.20 | 52001 | 93.184.216.34 | 80 | 192.168.1.20:52001 ↔ 93.184.216.34:80 | 203.0.113.50:50006 ↔ 93.184.216.34:80
192.168.1.20 | 52002 | 93.184.216.34 | 21 | 192.168.1.20:52002 ↔ 93.184.216.34:21 | 203.0.113.50:50007 ↔ 93.184.216.34:21
192.168.1.20 | 53001 | 74.125.200.108 | 993 | 192.168.1.20:53001 ↔ 74.125.200.108:993 | 203.0.113.50:50008 ↔ 74.125.200.108:993
192.168.1.20 | 53002 | 151.101.1.140 | 443 | 192.168.1.20:53002 ↔ 151.101.1.140:443 | 203.0.113.50:50009 ↔ 151.101.1.140:443
Notes: In the cloud lessons, you’ll see how crazy the port mappings can get.

## Slide 20: Questions